## Slide 1: Introduction
University of Bridgeport
<number>
Introduction to ROBOTICS
Notes: <number>

## Slide 2: Text Book
Mark W. Spong, Seth Hutchinson
and M. Vidyasagar, “Robot Modeling
and Control ” , Wiley , 2006
ISBN-10: 0471649902
ISBN-13: 978-0471649908

## Slide 3: Reference
Textbook
J. Craig, Introduction to Robotics: Mechanics and Control,” 2nd edition,
(ISBN: 0-201-52539-9).

## Slide 4: Topics Covered
Transformations.
Kinematics
Inverse kinematics
Jacobians
Trajectory generation
Robot control

## Slide 5: Definitions
Robot –A reprogrammable manipulator to perform specific mechanical functions such as move material and parts.
Robotics – the science dealing with design, construction and operation of robots

## Slide 6: Manipulators
Robot manipulators are composed of links connected by joints

## Slide 7: Joints
A joint is the connection between two or more links at their nodes.
It constrains the motions of the connected links.
A joint can be classified as:
  One-DOF
  Two-DOF
  Three-DOF
<number>
Notes: <number>

## Slide 8: One-DOF Joint
Revolute joint
Imposes a rotational motion
Symbol R
<number>
Notes: <number>

## Slide 9: One-DOF Joint
Prismatic joint
Imposes a translational motion
Symbol: P
<number>
Notes: <number>

## Slide 10: Two-DOF Joint
Universal joint
Symbol U
<number>
Notes: <number>

## Slide 11: Two-DOF Joint
Cylindrical joint
Symbol C
<number>
Notes: <number>

## Slide 12: Three DOF Joint
Ball-and-socket (spherical joint)
Symbol S
<number>
Notes: <number>

## Slide 13: Manipulators
<number>
Cartesian: PPP
Cylindrical: RPP
Spherical: RRP
RRP
(Selective Compliance Assembly Robot Arm)
Articulated: RRR
Hand coordinate:
n: normal vector; s: sliding vector;
a: approach vector, normal to the
tool mounting plate
Notes: <number>

## Slide 14: Configuration
A configuration of the manipulator is a complete specification of the location of every point on the manipulator.
If you know the values for the joint variable (joint angle for revolute joints or joint offset for prismatic joints), it is straightforward to infer the position of any point on the manipulator.
A configuration is represented by a set of values for the joint variable

## Slide 15: DOF
An object is said to have a n degrees of freedom (DOF), if its configuration can be minimally specified by n parameters.
For a robot manipulator, the number of joints determine the number of DOF.
To reach any point in the space with an arbitrary orientation: 6 DOF (3 DOF for positioning and 3 DOF for orientation)

## Slide 16: DOF
Less than 6 DOF: the arm cant reach any point in the space with an arbitrary orientation.
More than 6 DOF: Kinematically redundant manipulator.
Certain applications may require more than 6 DOF, for example:
  Obstacle Avoidance.

## Slide 17: Workspace
The Workspace of the manipulator is the total volume swept out by the end effector as the manipulator executes all possible motion.
Workspace is constrained by:
  Geometry of the manipulator.
  Mechanical constraint of the joints (a revolute joint may be limited to less than 360 degrees)

## Slide 19: Workspace
Reachable Workspace: the entire set of points reachable by the manipulator.
Dextrous Workspace: consists of those points that the manipulator can reach with an arbitrary orientation of the end effectors.
Dextrous Workspace is a subset of Reachable Workspace

## Slide 20: Performance Measure
Accuracy: is a measure of how close the manipulator can come to a given point within its workspace.
Repeatability: is a measure of how close the manipulator can return to a previously taught point.

## Slide 21: Wrist and End Effector
Wrist: the joints between the arm and the end effector.
Typically, the arm controls the position of the end effector, and the wrist controls the orientation.

## Slide 22: 3 DOF wrist
A typical wrist would have 3 DOF described as roll, pitch and yaw. Roll - rotation around the arm axis Pitch - up and down movement (assuming the roll is in its centre position) Yaw - right to left rotation (assuming the roll is in its centre position)

## Slide 23: End Effector
The device on the end of the arm, attached via the wrist, that performs the task, such as:
Grippers - Use to hold and move objects
Tools - Used to perform work on a part, not just to pick it up. A tool could be held by a gripper, making the system more flexible.