## Slide 1: Velocity Analysis Jacobian
University of Bridgeport
<number>
Introduction to ROBOTICS
Notes: <number>

## Slide 2: Kinematic relations
Joint Space
Task Space
θ =IK(X)
Location of the tool can be specified using a joint space or a cartesian space description
X=FK(θ)
Notes: <number>

## Slide 3: Velocity relations
Joint Space
Task Space
Relation between joint velocity and cartesian velocity.
JACOBIAN matrix J(θ)
Notes: <number>

## Slide 4: Jacobian
Suppose a position and orientation vector of a manipulator is a function of 6 joint variables: (from forward kinematics)
X = h(q)
Notes: <number>

## Slide 5: Jacobian Matrix
Forward kinematics
Notes: <number>

## Slide 6: Jacobian Matrix
Jacobian is a function of q, it is not a constant!
Notes: <number>

## Slide 7: Jacobian Matrix
Linear velocity
Angular velocity
The Jacbian Equation
Notes: <number>

## Slide 8: Example
2-DOF planar robot arm
  Given l1, l2 , Find: Jacobian
2
1
(x , y)
l2
l1

## Slide 9: Singularities
The inverse of the jacobian matrix cannot be calculated when
det [J(θ)] = 0
Singular points are such values of θ that cause the determinant of the Jacobian to be zero
Notes: <number>

## Slide 10
Find the singularity configuration of the 2-DOF planar robot arm
2
1
(x , y)
l2
l1
x
Y
=0
V
determinant(J)=0 Not full rank
Det(J)=0

## Slide 11: Jacobian Matrix
Pseudoinverse
  Let A be an mxn matrix, and let be the pseudoinverse of A. If A is of full rank, then can be computed as:
Notes: <number>

## Slide 12: Jacobian Matrix
  Example: Find X s.t.
Matlab Command: pinv(A) to calculate A+
Notes: <number>

## Slide 13: Jacobian Matrix
Inverse Jacobian
Singularity
  rank(J)<n : Jacobian Matrix is less than full rank
  Jacobian is non-invertable
  Boundary Singularities: occur when the tool tip is on the surface of the work envelop.
  Interior Singularities: occur inside the work envelope when two or more of the axes of the robot form a straight line, i.e., collinear
Notes: <number>

## Slide 14: Singularity
At Singularities:
  the manipulator end effector cant move in certain directions.
  Bounded End-Effector velocities may correspond to unbounded joint velocities.
  Bounded joint torques may correspond to unbounded End-Effector forces and torques.

## Slide 15: Jacobian Matrix
If
Then the cross product
Notes: <number>

## Slide 16: Remember DH parmeter
The transformation matrix T
Notes: <number>

## Slide 17: Jacobian Matrix
Notes: <number>

## Slide 18: Jacobian Matrix
2-DOF planar robot arm
  Given l1, l2 , Find: Jacobian
  Here, n=2,
2
1
(x , y)
l2
l1

## Slide 19
<number>
Where (θ1 + θ2 ) denoted by θ12 and
Notes: <number>

## Slide 20: Jacobian Matrix
2-DOF planar robot arm
  Given l1, l2 , Find: Jacobian
  Here, n=2
2
1
(x , y)
l2
l1

## Slide 21: Jacobian Matrix
Notes: <number>

## Slide 22: Jacobian Matrix
Notes: <number>

## Slide 23: Jacobian Matrix
The required Jacobian matrix J
Notes: <number>

## Slide 24
Stanford Manipulator
The DH parameters are:
Notes: <number>

## Slide 25
Stanford Manipulator
Notes: <number>

## Slide 26
Stanford Manipulator
T4 =
[ c1c2c4-s1s4, -c1s2, -c1c2s4-s1*c4, c1s2d3-sin1d2]
[ s1c2c4+c1s4, -s1s2, -s1c2s4+c1c4, s1s2d3+c1*d2]
[-s2c4, -c2, s2s4, c2*d3]
[ 0, 0, 0, 1]
Notes: <number>

## Slide 27
Stanford Manipulator
T5 =
[ (c1c2c4-s1s4)c5-c1s2s5, c1c2s4+s1c4, (c1c2c4-s1s4)s5+c1s2c5, c1s2d3-s1d2]
[ (s1c2c4+c1s4)c5-s1s2s5, s1c2s4-c1c4, (s1c2c4+c1s4)s5+s1s2c5, s1s2d3+c1d2]
[ -s2c4c5-c2s5, -s2s4, -s2c4s5+c2c5, c2d3]
[ 0, 0, 0, 1]
Notes: <number>

## Slide 28
Stanford Manipulator
T5 =
[ (c1c2c4-s1s4)c5-c1s2s5, c1c2s4+s1c4, (c1c2c4-s1s4)s5+c1s2c5, c1s2d3-s1d2]
[ (s1c2c4+c1s4)c5-s1s2s5, s1c2s4-c1c4, (s1c2c4+c1s4)s5+s1s2c5, s1s2d3+c1d2]
[ -s2c4c5-c2s5, -s2s4, -s2c4s5+c2c5, c2d3]
[ 0, 0, 0, 1]
Notes: <number>

## Slide 29
Stanford Manipulator
T6 = [ c6c5c1c2c4-c6c5s1s4-c6c1s2s5+s6c1c2s4+s6s1c4, -c5c1c2c4+s6c5s1s4+s6c1s2s5+c6c1c2s4+c6s1c4, s5c1c2c4-s5s1s4+c1s2c5, d6s5c1c2c4-d6s5s1s4+d6c1s2c5+c1s2d3-s1d2]
[ c6c5s1c2c4+c6c5c1s4-c6s1s2s5+s6s1c2s4-s6c1c4, -s6c5s1c2c4-s6c5c1s4+s6s1s2s5+c6s1c2s4-c6c1c4, s5s1c2c4+s5c1s4+s1s2c5, d6s5s1c2c4+d6s5c1s4+d6s1s2c5+s1s2d3+c1d2]
[ -c6s2c4c5-c6c2s5-s2s4s6, s6s2c4c5+s6c2s5-s2s4c6, -s2c4s5+c2c5, -d6s2c4s5+d6c2c5+c2d3]
[ 0, 0, 0, 1]
Notes: <number>

## Slide 30
Stanford Manipulator
Joints 1,2 are revolute
Joint 3 is prismatic
The required Jacobian matrix J
Notes: <number>

## Slide 31: Inverse Velocity
  The relation between the joint and end-effector velocities:
  where j (m×n). If J is a square matrix (m=n), the joint velocities:
  If m<n, let pseudoinverse J+ where
Notes: <number>

## Slide 32: Acceleration
  The relation between the joint and end-effector velocities:
  Differentiating this equation yields an expression for the acceleration:
  Given of the end-effector acceleration, the joint acceleration
Notes: <number>