## Slide 1: Trajectory Planning
University of Bridgeport
<number>
Introduction to ROBOTICS
Notes: <number>
<number>

## Slide 2: Trajectory planning
A trajectory is a function of time q(t) s.t. q(t0)=qs
And q(tf)=qf .
tf-t0 : time taken to execute the trajectory.
Point to point motion: plan a trajectory from the initial configuration q(t0) to the final q(tf). In some cases, there may be constraints (for example: if the robot must begin and end with zero velocity)

## Slide 3: Point to point motion
Choose the trajectory of polynomial of degree n , if you have n+1 constraints.
Ex (1):Given the 4 constraints: (n=3)

## Slide 4: Point to point motion
Cubic Trajectories
  4 coefficients (4 constraints)
  Define the trajectory q(t) to be a polynomial of degree n
  The desired velocity:

## Slide 5: Point to point motion
Evaluation of the ai coeff to satify the constaints

## Slide 6: Point to point motion
Combined the four equations into a single matrix equation.

## Slide 7: Point to point motion
Example

## Slide 8: Point to point motion
Cubic polynomial trajectory
Matlab code:
syms t;
q=10-90*t^2+60*t^3;
t=[0:0.01:1];
plot(t,subs(q,t))
xlabel('Time sec')
ylabel('Angle(deg)')

## Slide 9: Point to point motion
Velocity profile for cubic polynomial trajectory
Matlab code:
syms t;
qdot=-180*t+180*t^2;
t=[0:0.01:1];
plot(t,subs(qdot,t))
xlabel('Time sec')
ylabel(’velocity(deg/s)')

## Slide 10: Point to point motion
Acceleration profile for cubic polynomial trajectory
Matlab code:
syms t;
qddot=-180+360*t;
t=[0:0.01:1];
plot(t,subs(qddot,t))
xlabel('Time sec')
ylabel(’Acceleration(deg/s2)')

## Slide 11: HW 1
A single link robot with a rotary joint is at Ө=15ْ degrees. It is desired to move the joint in a smooth manner to Ө=75ْ in 3 sec. Find the coefficeints of a cubic to bring the manipulator to rest at the goal.

## Slide 12: HW2
The task is to take the end point of the RR robot from (0.5, 0.0, 0.0) to (0.5, 0.3, 0.0) in the X0Y0Z0 frame in a period of 5 seconds. Assume the robot is at rest at the starting point and should come to come to a complete stop at the final point.

## Slide 13: Example 2
Given the 6 constraints: (n=5)

## Slide 14: Point to point motion
Quintic Trajectories
  6 coefficients (6 constraints)
  Define the trajectory q(t) to be a polynomial of degree n
  The desired velocity:
  The desired acceleration:

## Slide 15: Point to point motion
Evalautation of the ai coeff to satify the constaints

## Slide 16: Point to point motion
Combined the six equations into a single matrix equation.

## Slide 17: Point to point motion
Combined the six equations into a single matrix equation.

## Slide 18: Linear segments with parabolic bends
We want the middle part of the trajectory to have a constant velocity V
  Ramp up to V
  Linear segment
  Ramp down